## Slide 1: LED Flashlight

## Slide 2: How does it work?
When electricity flows through an LED (light-emitting diode), the LED lights up
We need a battery, two LEDs, some wire, a switch and some know-how!

## Slide 3: Need to learn some things
How to read an electrical schematic
What parts we’re using
How to build the flashlight

## Slide 4: Reading Schematics:
Battery
What’s this?

## Slide 5: What’s this?
Diode
  Lets current flow one direction but not the other
YES
X
NO

## Slide 6: Electrical circuit
Must have a closed path all the way from one terminal of the battery to the other

## Slide 7: Will current flow?

## Slide 8: How about here?

## Slide 9: And here?

## Slide 10: Will current flow?

## Slide 11: How about now?

## Slide 12: Schematic versus real life
long lead is anode
anode
cathode

## Slide 13: Here’s our battery
Called a coin or button battery
This one is only 3 V
Hey, we don’t need a resistor then!
Notice the top is positive- that should connect to the anode (long lead)

## Slide 14: Are you ready to build?
Box
Coin battery
LED
3 pieces wire
Paper clip
Scissors, tape
Sandpaper
Lighter
Sticker
Marker

## Slide 15: Fold this flap and punch a hole through both layers

## Slide 16: LEDs: one lead is shorter!
If you forget which is shorter, look for the flat

## Slide 17: Color the top of the short lead

## Slide 18: Bend legs at the knees
Short!

## Slide 19: Got three pieces of magnet wire?

## Slide 20: Burn insulation off the ends
Then sand off the black stuff

## Slide 21: Twist one around the SHORT lead

## Slide 22: Use a pen or pencil to make a small loop in the other end

## Slide 23: Tape loop to bottom (-) side of battery

## Slide 24: Make a loop in another wire and tape it to the top (+) side of battery

## Slide 25: Here’s a chance to test it!
Touch the other end of the second wire to the other LED leads.
It should light up.
Touch, don’t twist!

## Slide 26: Find the THIRD wire
Twist one end to the unused LED leads
Wire ONE goes LED to battery
Wire TWO goes battery to nowhere right now
Wire THREE goes from LED to nowhere
Tape battery inside box

## Slide 27: Tape battery inside box
Poke LED out through the hole

## Slide 28: Bend the paper clip a little
Twist the end of the second wire to the paper clip

## Slide 29: Cover big loop of paper clip with tape
Tape to outside of box
Don’t cross fold in flap here

## Slide 30: Tape the big loop of the paper clip to the outside of the box
Cover the big loop with tape

## Slide 31: Get the last piece of wire
Slide one sanded end under the top part of the clip
This is going to be your switch!
Must be sanded part!!!

## Slide 32: Tape it down ONY THE END

## Slide 33: Thread the two wires from the switch to the inside
Tape it!
Test it! Close the switch! Does it light up?

## Slide 34: Fold up the box and put on the sticker!

## Slide 35: You are all done!